GKT
/system reset-configuration

RC: (Ligado na porta 23)

Tux2: (Ligado no switch na porta 7)
ifconfig eth1 172.16.111.1/24
route add -net 172.16.110.0/24 gw 172.16.111.253
route add -net 172.16.1.0/24 gw 172.16.111.254

sysctl net.ipv4.conf.eth1.accept_redirects=0
sysctl net.ipv4.conf.all.accept_redirects=0

[
route del -net 172.16.110.0/24 gw 172.16.111.253 (por netmask a seguir, acho que dá sem)
route add -net 172.16.110.0/24 gw 172.16.111.254

route add -net 172.16.110.0/24 gw 172.16.111.253 (por netmask a seguir, acho que dá sem)
route del -net 172.16.110.0/24 gw 172.16.111.254
]

sysctl net.ipv4.conf.eth1.accept_redirects=1
sysctl net.ipv4.conf.all.accept_redirects=1
//Perguntar stor ultima instruct slide 15
// e slide 16

Tux3: (Ligado no switch na porta 14)
ifconfig eth1 172.16.110.1/24
route add -net 172.16.111.0/24 gw 172.16.110.254
route add -net 172.16.1.0/24 gw 172.16.110.254

Tux4: (Ligado ao switch/router)(Ligado nas portas 21 22)
ifconfig eth1 172.16.110.254/24
ifconfig eth2 172.16.111.253/24
/interface bridge add name=bridge110
/interface bridge add name=bridge111
/interface bridge port remove [find interface=ether21] (Tux4 ligado na porta 21 do switch)
/interface bridge port remove [find interface=ether7] (Tux2 ligado na porta 7 do switch)
/interface bridge port remove [find interface=ether14] (Tux3 ligado na porta 14 do switch)
/interface bridge port add bridge=bridge110 interface=ether21
/interface bridge port add bridge=bridge110 interface=ether14
/interface bridge port add bridge=bridge111 interface=ether7
sysctl net.ipv4.ip_forward=1
sysctl net.ipv4.icmp_echo_ignore_broadcasts=0
/interface bridge port remove [find interface =ether22]
/interface bridge port add bridge=bridge111 interface=ether22
(trocar consola de switch para RC na porta 23)

/interface bridge port remove [find interface =ether23]
/interface bridge port add bridge=bridge111 interface=ether23
/system reset-configuration
/ip address add address=172.16.1.111/24 interface=ether1
/ip address add address=172.16.111.254/24 interface=ether2
route add -net 172.16.1.0/24 gw 172.16.111.254
/ip route add dst-address=172.16.110.0/24 gateway=172.16.31.253

[
/ip firewall nat disable 0
/ip firewall nat enable 0
]